## Slide 1
Real-time Speaker Recognizer
Offline and real-time speaker diarization system based on binary key modelling
Hao Pan Supervisor: Dr. Beta C.L. Yip
The University of Hong Kong, Faculty of Engineering, Department of Computer Science
Contact
References
Introduction
System Design
Real-time Version of the system:
VAD, Feature extraction, Feature binarization: Performed in online manner
KBM Training: Performed in offline manner, do not need to perform every time when data in.
Clustering: fast and naive online clustering first for new data, the result of offline clustering will be used to update the previous result when it complete
Resegmentation:
Discussion
Speaker diarization is the process of segmenting an input audio stream into speaker-homogeneous segments
Answer: “Who spoke when?”
Speaker identities and number of speakers are unknown
Speaker diarization ≠ Speaker recognition:
Timestamps are important
No enrollment process: no speaker voiceprint
Applications:
Improve ASR accuracy
Improve speaker recognition in multi-speaker data
Source separation: e.g. doctor vs patient
Spoken document indexing and retrieval
Generic diarization scheme:
Problem of existing system:
Require Intensive computation & long processing time
Online clustering performance are much worse than offline clustering
Lack of real-time application
Many system are domain-specific
Future Work
……
……
Acoustic features (MFCCs)
Sliding Windows
Gaussian
Pool
Select 1st Gaussian with max likelihood
Calculate cosine Dist with other Gaussians
Select Gaussian with biggest cosine distance
Stop when getting N Gaussians
most complementary & discriminant Gaussians
Speaker acoustic space
KBM
Count
Occurrences
N Gaussian Components
In KBM
n features vectors
For each feature, Gaussians that provide highest likelihood are chosen
…
…
……
1
15
7
3
25
5
17
…
Cumulative Vector (CV)
0
1
0
0
1
0
1
…
1 for top 20% values in CV, 0 otherwise
Binary Key (BK)
Segment/cluster representation
Features of segment
System flowchart
Input audio
MFCCs
(Acoustic features)
……
VAD (WebRTC)
VAD-mask
Feature extraction
Speech activity detection
Input audio
Segmentation
Segment/cluster representation
clustering
Resegmentation
Voice Activity Detection, Feature extraction
KBM Training
Feature Binarization
Clustering
Resegmentation
Visualization
Offline Clustering (Agglomerative clustering):
The cluster initialization
Cluster
Online Clustering:
In this project, we seek to develop a speaker recognizer system that
Language-independent, domain-robust, do not need prior training, and platform-independent
Be able to label the speakers in a recorded audio and visualize the results
Be able to generate outputs as the input is analyzed and correct the earlier output when necessary
Objectives
= 1 indicates the ith Gaussian coexist in the same region of acoustic space

## Slide 4
Feature extraction
Speech activity detection
Input audio
Segmentation
Segment/cluster representation
clustering
Resegmentation